## Slide 1
Topologies & cloud
Y13 - Cambridge International 9618 | 2.1.3 - 2.1.4
1
Notes: Follows the online lesson on 2.1.1-2.1.2 (LAN/MAN/WAN, client-server vs peer-to-peer, thin and thick clients). Starts with a closed-book recall test (worksheet Task 1). Exam questions used: 9618/11 Nov 2023 Q2, 9618/11 June 2024 Q5 and Q8, 9618/12 June 2024 Q3, 9618/13 June 2024 Q5.

## Slide 2
Recall test: last lesson
Starter activity
2
Last lesson was online. Let us check what stuck before we build on it.
Worksheet Task 1 covers... | Marks
LAN, MAN, WAN and PAN - size and description | 4
Benefits of networking computers | 3
Client-server or peer-to-peer? | 5
Exam question: client and server in an online bank (June 2024) | 4
Exam question: thin clients for online exam marking (June 2024) | 4
1
Closed book
No notes, no slides.
2
10 minutes
Then swap and mark.
Total: 20 marks. Be honest when you mark - it tells us what to revisit.
Notes: Closed book, 10 minutes, worksheet Task 1. Because last lesson was online, use the results to decide what to re-teach: anything below about half marks on Q3 or Q5 (client-server/peer-to-peer, thin/thick client) is worth a 5-minute recap before moving on. Two of the questions are real exam questions (June 2024 9618/11 Q5(a) and 9618/12 Q3(b)).

## Slide 3
In this lesson, you will
Objectives
3
Describe bus, star, mesh and hybrid topologies, and draw each one
Explain how packets are transmitted in each topology, including the difference between a hub and a switch
Give and explain advantages and disadvantages of each topology for a given scenario
Explain public, private and hybrid cloud, and the benefits and drawbacks of cloud storage
Answer real 9618 Paper 1 questions using the wording examiners reward

## Slide 4
What is a network topology?
Activity 1
4
A topology is the way the devices (nodes) in a network are arranged and connected to each other.
Bus
Star
Mesh
Hybrid
PC
PC
PC
switch
PC
PC
PC
PC
PC
PC
PC
PC
PC
PC
PC
switch
PC
PC
PC
PC
Notes: A topology is the arrangement of devices and the links between them. Ask: which of these have you seen? (School network: star of stars; the internet: mesh.)

## Slide 5
Bus topology
Activity 1
5
All devices connect to one shared central cable (the backbone). Terminators at each end stop signals bouncing back.
A
B
C
D
E
terminator
terminator
1
How a packet travels
A sends to D: the packet travels along the whole cable. Every node checks the destination address; only D accepts it.
Advantages | Disadvantages
Cheap: little cabling, no central device | If the backbone fails, the whole network fails
Easy to add another node | Collisions: only one device can transmit at a time
One failed node does not stop the others | Performance drops as traffic grows
 | Less secure: every packet passes every node
Notes: Every packet passes every node: each node checks the destination address and ignores packets not meant for it. Only one device can transmit at a time; simultaneous transmissions cause collisions (CSMA/CD - covered later). Terminators stop the signal reflecting back along the cable.

## Slide 6
Star topology
Activity 1
6
Every device has its own cable to a central device (usually a switch). All packets go through the central device.
switch
A
B
C
D
E
Advantages | Disadvantages
Fewer collisions: each device has its own link | If the switch fails, the whole network fails
One broken cable only affects one device | More cable, and a switch, so higher set-up cost
Easy to add or remove devices | 
More secure with a switch: packets go only to the destination | 
Easy to find faults | 
A sends to D: A -> switch, the switch reads the destination address, switch -> D only.
Notes: Official mark scheme wording (9618/13 June 2024 Q5(b)): the sending computer transmits packets directly to the switch/central device; the switch checks the destination address and forwards the packet directly to that device. Most school and office LANs are stars.

## Slide 7
Star: hub or switch in the middle?
Activity 1
7
Hub: sends every packet to every device
A
B
C
D
hub
Switch: sends each packet only to its destination
A
B
C
D
switch
A sends a packet to D. With a hub, B, C and D all receive it (B and C ignore it). With a switch, only D receives it.
Notes: Hubs are not in the 9618 syllabus as hardware to describe, but the comparison explains why a star with a switch is more secure and has fewer collisions. A star with a hub behaves like a bus: every packet reaches every node.

## Slide 8
Mesh topology
Activity 1
8
Devices are interconnected so there are many routes between any two nodes. Data can be re-routed if a link fails.
A
B
C
D
E
Advantages | Disadvantages
Multiple paths: a broken link does not stop the network | Lots of cabling - expensive (wired mesh)
Data can take the best/shortest route | Complex to set up and maintain
Handles heavy traffic well | 
Good privacy: packets follow dedicated routes | 
1
Routing vs flooding
Routing: nodes choose the best route. Flooding: data is sent through every node.
Notes: Routing mesh: nodes act like routers and send data by the best route, re-routing round failed links. Flooding mesh: data is sent to every node (no routing logic) - simple but creates extra traffic. The internet and many WANs are mesh networks.

## Slide 9
Hybrid topology
Activity 1
9
A combination of two or more topologies, e.g. star networks joined by a bus backbone.
Office
PC
PC
PC
Labs
PC
PC
PC
Server
bus backbone
1
Advantages
Joins existing networks without rebuilding them. Handles large traffic volumes. Well suited to large networks; easy to expand.
2
Disadvantage
Complex to install, configure and maintain. Other pros and cons depend on the topologies used.
Example: a company buys three hotel chains that use bus, star and mesh networks, and joins them into one hybrid network.
Notes: Textbook example: three hotel chains using bus, star and mesh networks are taken over by one company and joined into a single hybrid network. Advantages and disadvantages depend on the topologies combined; the extra disadvantage is complexity.

## Slide 10
Comparing the topologies
Activity 2
10
 | Bus | Star | Mesh
Devices connect to... | one shared central cable | one central device (switch) | several other devices
Paths between two nodes | one (the backbone) | one (through the switch) | many
Single point of failure | the backbone cable | the switch | none
Collisions | most likely | fewer (switch) | few
Who sees each packet | every node | only the destination (switch) | nodes on the route
Cost | lowest | medium | highest (wired)
Typical use | small, light-traffic networks | most school / office LANs | the internet, WANs, sensor networks
Notes: This is exactly the knowledge tested by the June 2024 9618/11 Q8(a) tick-box question (worksheet Task 3). Students should be able to justify each cell.

## Slide 11
Exam focus: packets in a star
Activity 2
11
June 2024 (9618/13) Q5(b): Explain how packets are transmitted between two devices in a star topology. [2]
Mark | Marking point (official)
1 | The sending computer transmits the packet directly to the switch / central device
1 | The switch checks the destination address of the packet and forwards it directly to that device
Nov 2023 (9618/11) Q2(d): 20 computers and a switch. Explain one advantage of a star instead of a bus. [2]
Advantage (1 mark) | ... expansion (1 mark)
More resilient to faults | no single shared cable, so less disruption to teaching
Higher performance as fewer collisions | each device is only connected to the switch
Easier to add new nodes | each device connects directly to the switch
Easier to find faults than in a bus | 
Notes: Show after students attempt worksheet Task 4. Official marking points from 9618/13 May/June 2024 Q5(b) [2] and 9618/11 Oct/Nov 2023 Q2(d) [2]. Note the 2-mark "explain" pattern: a point, then an expansion that applies it to the scenario.

## Slide 12
Think, pair, share
Activity 2
12
Choose the best topology for each scenario, and justify it with one advantage that is relevant to that scenario.
1
A school ICT suite with 30 PCs
2
Sensors monitoring patients across a hospital
3
A small temporary office with 4 laptops and light traffic
Exam tip: "Explain" = make the point, then say why it matters in THIS scenario.
Notes: Good answers: Star - a school ICT suite (cheap switch, easy to add PCs, one cable fault only affects one PC). Mesh - a hospital patient-monitoring sensor network or a bank WAN (no single point of failure, re-routing). Bus - a small temporary office with light traffic (cheapest).

## Slide 13
Cloud computing and cloud storage
Activity 3
13
Cloud storage: data is stored on off-site servers, owned and managed by a hosting company, and accessed over the internet.
internet
Laptop
Phone
Tablet
server
server
server
same data copied on several servers = data redundancy
1
Redundancy
The same data is stored on more than one server, so it is still available if one is down for maintenance or repair.
Cloud computing also includes cloud software: applications hosted and maintained by the provider and used through a browser or app.
Notes: Cloud storage is one part of cloud computing (others: cloud software, databases, analytics). Data redundancy: the same data is kept on more than one server so it is still available during maintenance, repair or failure.

## Slide 14
Public, private and hybrid cloud
Activity 3
14
 | Public cloud | Private cloud | Hybrid cloud
Who provides it | A third-party provider (a different company) | Dedicated to one organisation, behind its firewall | A mix of both
Who can use it | Anyone who pays / signs up | Only that organisation | Sensitive data private; the rest public
Control of security & backup | The provider | The organisation | Split
Cost | Low start-up; pay as you go | High start-up and running costs | In between
Example | Students saving work to a free cloud drive | A bank storing customer records | A hospital: patient records private, public website files public
Learn the private cloud definition: storage/services on a remote server dedicated to, and only available to, one company.
Notes: Official definition of private cloud (9618/13 June 2024 Q5(a)(i)): dedicated / bespoke services or storage on a remote server only available to the company. Public cloud: the customer and the cloud provider are different companies; services are offered to anyone over the internet.

## Slide 15
Benefits and drawbacks of cloud storage
Activity 3
15
Benefits | Drawbacks
Access files from any device, anywhere, with internet access | No access without a reliable internet connection
No need to carry storage devices | Free space is limited - more storage must be paid for
Remote backup helps disaster recovery | Users depend on a third party for security and backups
Data redundancy keeps data available | Large uploads/downloads use data allowance
Almost unlimited, scalable capacity | If the provider fails, data could be lost
Provider handles maintenance and upgrades | Hacking of accounts / data breaches
Notes: Exam answers must be specific: "needs internet" alone is weak; "cannot access their files without a reliable internet connection" earns the mark (Nov 2023 9618/11 Q2(c)).

## Slide 16
Security and data loss in the cloud
Activity 3
16
A company that moves its data to a public cloud gives up direct control of its data security.
1
Physical security
How well protected is the building that houses the servers?
2
Disasters
How resilient is the provider to fires, floods and outages?
3
Staff and hackers
Could provider staff or hackers access confidential data?
Real incidents: a provider permanently lost customer data during a routine backup; hacked cloud accounts leaked private photos; 93 million voter records were exposed in 2016.
This is why organisations with sensitive data often choose a private or hybrid cloud.
Notes: Textbook examples: the XEN hypervisor flaw forced providers to reboot servers; a provider permanently lost data during a routine backup; celebrity photo leaks from hacked cloud accounts; 93 million Mexican voter records exposed (2016). Use these to discuss why a bank might choose a private cloud.

## Slide 17
Exam focus: cloud questions
Activity 3
17
June 2024 (9618/13) Q5(a)(ii): benefits to a company of private instead of public cloud storage. [3]
Marking point (official, any 3)
Not reliant on a third party ...
... gives greater control over security / privacy
... gives greater control over backup
Storage can be tailored / scaled to the company's requirements
Nov 2023 (9618/11) Q2(c): two drawbacks of students storing files on a public cloud. [2]
Marking point (official, any 2)
Cannot access their files without a reliable internet connection
Free space may be limited, so they may have to buy more
No control over backup / security - dependent on a third party
Notes: Show after students attempt worksheet Task 5. Official marking points: 9618/13 May/June 2024 Q5(a)(ii) [3] and 9618/11 Oct/Nov 2023 Q2(c) [2].

## Slide 18
Guided practice
Activity 4
18
Task 2: draw bus and star networks, and identify topologies from descriptions
Task 3: the June 2024 tick-box question, then trace a packet through a bus, a hub and a switch
Task 4: real exam questions on topologies (Nov 2023, June 2024)
Task 5: real exam questions on public and private cloud
Task 6 (extension): peer-to-peer vs mesh, and choosing a cloud for a scenario
Check your work against the answer key when your teacher shares it
Notes: Task 1 was the recall test. Tasks 2-5 on paper (about 30 minutes); Task 6 extension. Show slides 11 and 17 after Tasks 4 and 5 so students can self-mark against the official points.

## Slide 19
Common misconceptions
Plenary
19
Misconception | Why it is wrong
"In a star, packets go to every computer." | Only with a hub. A switch checks the destination address and forwards to that device only.
"A star has no single point of failure." | If the central switch fails, the whole network fails.
"Mesh means peer-to-peer." | Mesh is a physical layout of links; peer-to-peer is a model of how nodes share resources.
"Private cloud means storing data on your own computer." | It is still remote server storage - but dedicated to one organisation only.
"The cloud needs internet" is enough for the mark. | Be specific: users cannot access files without a reliable internet connection.

## Slide 20
Exit question
Plenary
20
A medical clinic is setting up a new LAN with 15 computers. It also needs to store confidential patient records.
1. Which topology would you recommend for the LAN? Explain one advantage for the clinic. [2]
2. Should the patient records be stored on a public or a private cloud? Justify your answer. [2]
Notes: Model answer: Star (1). Each laptop/device has its own connection to a switch, so one faulty cable only affects one device // the switch only forwards packets to the destination so fewer collisions and better performance (1 for expansion). Private cloud (1) because patient records are confidential: the clinic is not reliant on a third party and has greater control over security/privacy (1).

## Slide 21
In this lesson, you
Summary
21
Checked your recall of LANs/WANs, client-server and thin/thick clients
Described and drew bus, star, mesh and hybrid topologies
Explained how packets travel in each topology, and why a switch beats a hub
Compared public, private and hybrid cloud, and the benefits and drawbacks of cloud storage
Answered real 9618 Paper 1 questions using the official marking points
Next lesson: 2.1.5 - wired and wireless networking (Wi-Fi, Bluetooth and cables).