## Slide 1
Wired & wireless
Y12 - Cambridge International 9618 | 2.1.5
1
Notes: Short lesson (about 30 minutes): recall test 5 min, teaching 12 min, tasks 12 min, exit 1 min. Task 4 (the 20-floor building) is extension or homework.

## Slide 2
Recall test: topologies & cloud
Starter activity
2
Worksheet Task 1 covers... | Marks
Name the topology from a description (bus, star, mesh) | 3
Define private cloud | 1
Exam question: public cloud vs a server on a LAN (Nov 2023) | 4
1
Closed book
No notes, no slides.
2
5 minutes
Then swap and mark.
Total: 8 marks.
Notes: Worksheet Task 1, closed book, 5 minutes. Q3 is a real exam question: 9618/13 Oct/Nov 2023 Q3(a)(ii). If most students drop marks on Q3, spend 2 minutes on the "point + expansion" pattern before moving on.

## Slide 3
In this lesson, you will
Objectives
3
Compare Wi-Fi and Bluetooth, and explain spread spectrum frequency hopping
Compare radio waves, microwaves and infrared, and explain why satellites are needed
Compare twisted pair, coaxial and fibre-optic cables
Recommend wired or wireless connectivity for a scenario, with reasons

## Slide 4
Wireless: electromagnetic radiation
Activity 1
4
Wireless networks carry data using electromagnetic radiation: radio waves, microwaves or infrared.
 | Radio waves | Microwaves | Infrared
Bandwidth (data it can carry) | lowest | medium | highest
Penetration (through walls) | best | medium | worst - easily blocked
Range | longest | medium | about 1-2 metres
Typical use | broadcasting, long range links | Wi-Fi, satellite links | TV remotes, short indoor links
Microwaves are the best compromise: reasonable bandwidth, penetration and range.
Notes: Textbook Table 2.5. Simplify for students: radio waves go furthest and through walls; infrared carries the most data but is easily blocked (indoor only - which also stops it interfering elsewhere); microwaves are the compromise, which is why Wi-Fi uses them.

## Slide 5
Wi-Fi vs Bluetooth
Activity 1
5
 | Wi-Fi | Bluetooth
Range | up to about 100 m from a WAP / hotspot | less than about 30 m
Data transfer rate | much faster | slower - speed not critical
Security | better (e.g. WPA2 encryption) | key encryption
Creates a... | WLAN - a full-scale network | WPAN - devices close to one person
Typical use | laptops and phones on a school or home network | phone to headset, phone to speaker
Standard / frequency | IEEE 802.11 | 79 channels around 2.45 GHz
Choose Bluetooth for low-bandwidth links between nearby devices; choose Wi-Fi for a whole network.
Notes: Both use radio waves / spread spectrum. Bluetooth creates a WPAN (wireless personal area network) using key encryption. Wi-Fi implements the IEEE 802.11 protocols and is designed for full networks through wireless access points.

## Slide 6
Bluetooth: frequency hopping
Activity 1
6
A device picks one of 79 channels at random. If it is in use, it picks another - and pairs keep hopping channels several times a second.
ch 7
1
2
ch 6
2
1
ch 5
1
2
1
ch 4
1
2
ch 3
2
1
ch 2
2
1
2
ch 1
1
2
time ->
1
Pair 1 (navy)
e.g. phone and headset
2
Pair 2 (yellow)
e.g. laptop and mouse
The pairs never use the same channel at the same time, so they do not interfere.
Notes: Each communicating pair picks one of the 79 channels at random; if it is in use, it picks another. Pairs also hop between channels several times a second, so two pairs rarely clash and interference is minimised. In the grid, pair 1 and pair 2 never use the same channel at the same time.

## Slide 7
Why do we need satellites?
Activity 1
7
A
B
satellite
blocked by the Earth's curve
1
The problem
Signals travel in straight lines, so the curvature of the Earth stops a signal from A reaching a distant antenna B.
2
The solution
A beams the signal up to a satellite, which boosts it and beams it back down to B.
3
How
Radio or microwave frequencies, with different frequency bands to stop interference.
Notes: Radio and microwave signals travel in straight lines, so the curvature of the Earth blocks a signal between two distant antennae. A satellite receives the signal, boosts it and beams it back down. Different frequency bands are used to avoid interference.

## Slide 8
Wired: three types of cable
Activity 2
8
 | Twisted pair | Coaxial | Fibre optic
Carries data as... | electrical signals (copper) | electrical signals (copper core) | pulses of light (glass fibres)
Cost | cheapest | medium | most expensive
Data transfer rate | lowest | medium (about 80x twisted pair) | highest (about 26 000x)
External interference | affected most | affected less | very high resistance
Typical use | most LANs (Ethernet) | MANs, cable TV | long distances, WAN / internet backbones
Fibre: best data transfer rate, smallest signal loss over distance, immune to electrical interference - but the most expensive.
Notes: Textbook figures: coaxial has about 80 times, and fibre about 26 000 times, the transmission capacity of twisted pair. Shielded twisted pair has a metal foil jacket to cancel some interference; unshielded is used at home.

## Slide 9
Fibre optic: single-mode and multi-mode
Activity 2
9
Single-mode
Small core, single light path, little reflection
Data travels faster and further. Used for telecommunications and cable TV.
Multi-mode
Larger core, light reflects many times
Works best over shorter distances, e.g. within a LAN.
Notes: Keep this brief - it is a one-line distinction in the textbook. Single-mode: smaller core, less reflection, so faster and further (telecoms, cable TV). Multi-mode: larger core, more reflections, so best over short distances such as within a LAN.

## Slide 10
Wired or wireless?
Activity 2
10
Wireless | Wired
+ Easy to expand - no cables to install | + More reliable and stable - less interference
+ Devices are mobile within range of the WAPs | + Faster data transfer, no "dead spots"
- More interference from external sources | + Tends to be cheaper overall
- Less secure: signals can be intercepted, so encrypt (e.g. WPA2) | - Devices are not mobile
- Slower data transfer rate | - Trip hazards, overheating, cables pulled out
- Signals blocked by thick walls; strength can drop out | - May need permission to lay cables underground
Also consider: phones and tablets need Wi-Fi or Bluetooth; some countries restrict wireless frequencies.
Notes: These are the textbook points. In exam answers, make each point comparative ("faster than wireless") and apply it to the scenario.

## Slide 11
Exam technique: "recommend and justify"
Activity 3
11
1
Point
State the advantage or disadvantage, comparing the two options: "Wired is faster than wireless..."
2
Expansion
...apply it to the scenario: "...so staff on every floor can access the file server quickly."
3
Conclusion
Make a decision and justify it - a mixed solution is allowed: "Wired backbone with Wi-Fi on each floor, because..."
A list of single words ("faster", "secure") earns little. Point + expansion applied to the scenario earns the marks.
Modelled together - one point for a 20-floor office building:
Point | Expansion (applied to the scenario)
Wired connections give faster, more stable data transfer than wireless | ...so staff on all 20 floors can open large files on the server without slowdowns or drop-outs
Notes: Use for Task 4 (textbook Activity 2B Q4: a 20-floor building). The structure earns marks; the content is from slide 10. Model one point together, e.g. "Wired connections give faster data transfer than wireless, so staff on all 20 floors can access the file server without slowdowns."

## Slide 12
Misconceptions and exit question
Plenary
12
Misconception | Why it is wrong
"Bluetooth and Wi-Fi are the same." | Bluetooth: short range (< 30 m), low bandwidth, WPAN. Wi-Fi: about 100 m, faster, full networks.
"Fibre carries electricity very fast." | Fibre carries pulses of light, which is why it is not affected by electrical interference.
"Wireless is always cheaper." | Wired tends to be cheaper overall, despite the cost of buying and installing cable.
Exit: Two school buildings are 2 km apart. Which cable should connect them? Give one reason. [2]
Next lesson: 2.1.6 - hardware requirements of networks (switch, router, WAP, bridge, NIC, modem).
Notes: Exit answer: fibre optic (1) - the highest data transfer rate // the least signal loss over 2 km // not affected by electrical interference (1). Accept: twisted pair loses too much signal over that distance.